## Slide 1: PET segmentation & MICCAI challenge
Baptiste Laurent
Laboratory of Medical Information Processing
LaTIM INSERM-UBO UMR 1101, Brest

## Slide 2: Introduction
Segmenting PET images
PET segmentation
  Estimate volumes and boundaries of abnormal tissues
Applications
  Survival prognostic
  Radiotherapy planning
  Therapy monitoring
  Radiomics / tumor characterization

## Slide 3: Introduction
Segmenting PET images: the need for accuracy
Hatt, et al. Prognostic value of 18F-FDG PET image-based parameters in oesophageal cancer and impact of tumour delineation methodology. Eur J Nucl Med Mol Imaging 2011
Stratification of patients according to volume
  Accuracy not very important
    Only need to preserve hierarchy between patients
cm3
cm3
cm3
cm3
Fuzzy locally adaptive bayesian (FLAB)
Adaptive thresholding

## Slide 4: Introduction
Segmenting PET images: the need for accuracy
Radiotherapy planning
  Accuracy very important
    Sensitivity > positive predictive value
Le Maitre, et al. Impact of the accuracy of automatic tumour functional volume delineation on radiotherapy treatment planning. Phys Med Biol 2012

## Slide 5: Introduction
Segmenting PET images: the need for accuracy
Therapy monitoring
  Accuracy very important
    Positive predictive value > sensitivity
Hatt, et al. Early prediction of pathological response in locally advanced rectal cancer based on sequential 18F-FDG PET. Acta Oncol 2013

## Slide 6: Introduction
Segmenting PET images: the need for accuracy
Radiomics / tumor characterization
  Accuracy could be very important
    Especially for shape descriptors
    Some textural features are also highly sensitive
M. Hatt, et al. Tumor functional sphericity from PET images: prognostic value in NSCLC and impact of delineation method. Eur J Nucl Med Mol Imaging (in press) 2017
M. Hatt, et al. Robustness of intratumour ¹⁸F-FDG PET uptake heterogeneity quantification for therapy response prediction in oesophageal carcinoma. Eur J Nucl Med Mol Imaging 2013

## Slide 7: Introduction
PET image segmentation: challenges

## Slide 8: Introduction
PET direct segmentation
PET image segmentation: challenges
Limited signal-to-noise ratio
(sensitivity, acq. duration…)
Partial volume effects
(spatial resolution ~ 5 mm FWHM)
Spatial sampling
(voxel size ~ 2 – 5 mm)
Uptake heterogeneity
Range of shape complexity
M. Hatt, et al. Metabolically active volumes automatic delineation methodologies in PET imaging: Review and perspectives. Cancer Radiother 2011
J.A. Lee. Segmentation of positron emission tomography images: some recommendations for target delineation in radiation oncology. Radiother Oncol. 2010
Manual segmentation unreliable (high intra and inter variability)
There is no single threshold value adequate for all cases
Binary segmentation can be insufficient

## Slide 9: The era of thresholding
1997-2007
  One of the first papers (conference)
    Suggested the use of a fixed threshold of 42% of the max for most cases (except extreme ones)
  Numerous subsequent papers for thresholding1
    Suggested other fixed threshold values
      between 30 and 80% of SUVmax / SUVpeak
      >SUV 2.5, 2.0 …
    Extended the paradigm to « adaptive » thresholding
      Iterative approaches
      Taking into account the background value and/or contrast
      Usually require optimization using phantom acquisitions
        For each scanner model
        For each acquisition protocol
A.-S. Dewalle-Vignion, et al. Les méthodes de seuillage en TEP : un état de l’art. Médecine Nucléaire 2010

## Slide 10: Thresholding: limitations
Fixed and adaptive thresholding
M. Hatt. Automatic determination of functional volumes for oncology applications. PhD thesis, University of Brest 2008.

## Slide 11: The era of image segmentation
2007 and beyond
  Two « landmark » papers in 2007

## Slide 12: The era of image segmentation
2007 and beyond
After 2007: surge of publications
B. Foster, et al. A review on segmentation of positron emission tomography images. Comput Biol Med. 2014

## Slide 13: The era of image segmentation
State-of-the-art
  Categories of methods
Foster B, et al. A review on segmentation of positron emission tomography images. Comput Biol Med. 2014

## Slide 14: The era of image segmentation
State-of-the-art
  Categories of methods
B. Foster, et al. A review on segmentation of positron emission tomography images. Comput Biol Med. 2014

## Slide 15: The era of image segmentation
State-of-the-art
  Categories of methods
B. Foster, et al. A review on segmentation of positron emission tomography images. Comput Biol Med. 2014

## Slide 16: The era of image segmentation
State-of-the-art
  Categories of methods
B. Foster, et al. A review on segmentation of positron emission tomography images. Comput Biol Med. 2014

## Slide 17: PET segmentation
State-of-the-art
  Until recently:
    A large number of studies trying to optimize some kind of basic binary threshold (iterative methods, etc.)
    Existing image segmentation paradigms simply applied and/or adapted to PET or PET/CT
    In both cases validation often insufficent / incomplete
    Implementation by vendors is limited (some popular approaches such as region growing, adaptive thresholding, gradient-based…)
M. Hatt, et al. Classification and evaluation strategies of auto-segmentation approaches for PET: Report of AAPM task group No. 211. Med Phys. 2017

## Slide 18: PET segmentation
State-of-the-art
  Until recently:
    User intervention remains crucial
      To identify and/or isolate the object of interest
      Sometimes to initialize parameters (seeds, etc.)
      To validate and/or edit the result
  Recent developments towards:
    Consensus / ensemble techniques
    Machine learning
    Multimodal (PET/CT, PET/MR, PET/CT/MR) methods
M. Hatt, et al. Classification and evaluation strategies of auto-segmentation approaches for PET: Report of AAPM task group No. 211. Med Phys. 2017

## Slide 19: AAPM Task group 211
Creation and objectives
  Task Group No. 211 - Classification, Advantages and Limitations of the Auto-Segmentation Approaches for PET
  Started 2011
  Objectives :
    Review the state of the art
    Evaluate critically both methods and their evaluation
    Propose a benchmark and evaluation methodology guidelines
http://www.aapm.org/org/structure/default.asp?committee_code=TG211

## Slide 20: AAPM Task group 211
Motivation and context
TG 211 report 1
    “Given the large number of published PET-AS algorithms, their different level of validation and because most of these published algorithms are not yet implemented in commercially available software, the selection of one recommended method is challenging and premature”
Hatt, et al. Classification and evaluation strategies of auto-segmentation approaches for PET. Report of the American Association of Physicists in Medicine Task group 211. Med Phys. 2016 (in press)

## Slide 21: AAPM Task group 211
Motivation and context
TG 211 report 1
    “Clearly, further research (…) is needed, and one potential solution for going forward is the creation of a standardized protocol (i.e., a benchmark) (…)
    the benchmark needs to consist of several image datasets of different types: experimental (phantoms), numerically simulated and clinical, in order to compensate for the deficiencies of each of them (…). The performance of the methods needs to be evaluated using different metrics (…)”
Hatt, et al. Classification and evaluation strategies of auto-segmentation approaches for PET. Report of the American Association of Physicists in Medicine Task group 211. Med Phys. 2016 (in press)

## Slide 22: PET segmentation challenge
Previous challenges
  Quantitative Imaging Network (QIN) PET Segmentation Challenge1
    Only phantom data (available through TCIA website)
    No update since 10/2013
  Turku PET Centre contouring challenge2
    Numerous methods but limited amount of images (only 1 phantom)
    Focus on radiotherapy treatment planning
  No MICCAI challenge on PET image segmentation
1. http://michallenges.org/petSegmentationChallenge/
2. Shepherd, et al. Comparative study with new accuracy metrics for target volume contouring in PET image guided radiation therapy. IEEE Trans Med Imaging. 2012

## Slide 23: PET segmentation challenge
Objectives of the first MICCAI PET challenge:
  1. Evaluate and compare methods accuracy with rigorously chosen performance metrics
  2. Provide large datasets of various images types with rigorous ground truth
  3. Provide an online platform to run and evaluate methods, to reach an objective and standardized evaluation protocol.

## Slide 24
FLI@Compute
FLI-IAM Web portal
XDS/XCA
Information
System and
Search Engine
Metadata
Catalogs
FLI@Interoperability
FLI@compute
Submission
FLI@Access
(instance 1)
Private
servers
(Psychiatry)
Onto
Neurolog
LAN
ArchiMed
Private
servers
(Oncology)
LAN
Private
servers
(instance 2)
(MS)
Onto
Neurolog
LAN
CATIdb
Private
servers
(Memory)
LAN
(MOTEUR)
VIP
OntoVIP
Internet
PC
MedInria
(ITK/ANIMA)
(BrainVisa)
BRAINVisa
PC
CATI (capsul)
Private
clusters
(BrainVisa)
LAN
Black
Board
CARMIN
API
PET Challenge
IAM Computing/Data Architecture

## Slide 25: PET segmentation challenge
Platform architecture
M. Hatt, et al. The first MICCAI challenge on PET tumor segmentation. Medical Image Analysis 2018
Training / Testing
Total:
9 / 66
6 / 70
19 / 157
4 / 21

## Slide 26: PET segmentation challenge
Registered participants
  5/12 explained not having the time/manpower to take care of the pipeline integration, no answer from the 7 others.
  Perhaps some renounced based on results obtained on the training set?
Organization details, participants
Steps | Number of participants | Number of pipelines
Registration and download of training data | 16 | 
Submission of a paper | 4 | 
Pipelines integration and testing data | 4 | 10

## Slide 27: PET segmentation challenge
M. Hatt, et al. The first MICCAI challenge on PET tumor segmentation. Medical Image Analysis 2018
13 methods were compared (10 challengers and 3 reference methods : FLAB, T40, T50)
ACO(s) and (d) = ant colony algorithm with static or dynamic initialization
  Fayad, et al. J Nucl Med 2015;56:1745
ARG = adaptive region growing + curvature strategy
  Tan, et al. Med Phys 2017;62:5383-5402
CNN = convolutional neural network (using only the available training data)
  Krizhevsky, et al. Advances in neural information processing systems 2012;1097-1105
DICT = dictionary model (+ pre/post-processing for noise/morphology)
  Dahl & Larsen. British Machine Vision Conference 2011
FLAB = fuzzy locally adaptive Bayesian
Hatt, et al. IEEE Trans Med Imaging 2009;28:881-893
GARAC = gradient-aided region-based active contour
Jaouen, et al. IEEE NSS-MIC 2016
GMM = gaussian mixture model (+ pre/post-processing for noise/morphology)
Aristophanous, et al. Med Phys 2007;34:4223-4235
KM = k-means (+ pre/post-processing for noise/morphology)
Arthur & Vassilvitskii. ACM-SIAM Symposium on Discrete Algorithms 2007
SDWFCM = spatial-distance weighted fuzzy c-means (+ pre/post-processing for noise/morphology)
  Guo, et al. Wseas Trans. Comput. 2015;14:369-381
RF = random forest on image features (incl. textures)
Breiman, et al. Mach. Learn. 2001;45;5-32
T40 and T50 = threshold at 40 and 50% of max
Evaluated methods

## Slide 28: PET segmentation challenge
Datasets: 3 types of data (19 training - 149 testing)
Data and evaluation protocol
Clinical images
Physical phantoms
Numerical phantoms (Monte Carlo)
Analytical simulations
JF. Daisne, et al. Radiology 2004
T. Shepherd, et al. IEEE TMI 2012
M. Hatt, et al. IJROBP 2010
J. Lapuyade-Lahorgue, et al. Med Phys 2015
F. Zito, et al. Med Phys 2012
B. Berthon, et al. Med Phys 2014
A. Le Maitre, et al. Proceedings of the IEEE 2009
P. Papadimitroulas, et al. Med Phys 2013
M. Aristophanous, et al. Phys Med 2008
B. Berthon, et al. Phys Med. 2015
N=25
N=66
N=95 (18 testing excluded)

## Slide 29: PET segmentation challenge
Datasets: 3 types of associated ground-truth
Digitized histopathology
Consensus of multiple expert delineations
Truth masks of sub-voxel precision from thresholding of associated CT
Absolute truth as used in image generation
Clinical images
Physical phantoms
Simulations
  Monte Carlo
  Analytical simulations
Data and evaluation protocol

## Slide 30: PET segmentation challenge
Type of data and ground-truth
Clinical images
Physical phantoms
Simulations
Data and evaluation protocol
Reliability of ground-truth
Realism of data/image
Surrogate of truth only
Real cases
Reliable ground-truth with some limitation
Real acquisitions of simplistic objects
Very reliable ground-truth
Simulations with varying levels of realism in both object and image generation

## Slide 31: PET segmentation challenge
M. Hatt, et al. Report of AAPM TG211: Classification and evaluation strategies of auto-segmentation approaches for PET. Med Phys 2017
Evaluation metrics

## Slide 32: PET segmentation challenge
Statistical analysis
  Comparison of metrics distributions (not normal) using Mann-Whitney rank-sum test
Data and evaluation protocol
Metric
Method 1
Method 2
75 percentile
25 percentile
Median
Min
Max
Outside value
< or > lower/upper quartile ± 1.5 × interquartile range
Far out value
< or > lower/upper quartile ± 3 × interquartile range

## Slide 33: PET segmentation challenge
Visual examples – agreement on clinical image
Results for best methods of each team
Original PET
ACO
ARG
Surrogate of truth
GARAC
CNN

## Slide 34: PET segmentation challenge
Visual examples – agreement on phantom image
Results for best methods of each team
Original PET
ACO
ARG
Ground-truth
GARAC
CNN

## Slide 35: PET segmentation challenge
Visual examples – agreement on simulated image
Results for best methods of each team
Original PET
ACO
ARG
Ground-truth
GARAC
CNN

## Slide 36: PET segmentation challenge
Visual examples – disagreement on clinical image
Results for best methods of each team
Original PET
ACO
ARG
Surrogate of truth
GARAC
CNN

## Slide 37: PET segmentation challenge
Visual examples – disagreement on phantom image
Results for best methods of each team
Original PET
ACO
ARG
Ground-truth
GARAC
CNN

## Slide 38: PET segmentation challenge
Visual examples – disagreement on simulated image
Results for best methods of each team
Original PET
ACO
ARG
Ground-truth
GARBAC
CNN

## Slide 39: PET segmentation challenge
M. Hatt, et al. The first MICCAI challenge on PET tumor segmentation. Medical Image Analysis 2018
Results
  Sensitivity Positive Predictive Value (PPV)

## Slide 40: PET segmentation challenge
M. Hatt, et al. The first MICCAI challenge on PET tumor segmentation. Medical Image Analysis 2018
Results
  Accuracy (mean of SE and PPV)

## Slide 41: PET segmentation challenge
Metrics according to applications
  If we assume
    SE is more important than PPV for radiotherapy planning (gross tumor volume definition)
    PPV is more important than SE for response assessment (extraction of quantitative metrics)
Results
Application | SE | PPV
Pure segmentation (this challenge) | 0.5 | 0.5
Radiotherapy planning | 0.6 | 0.4
Therapy follow-up | 0.4 | 0.6

## Slide 42: PET segmentation challenge
Metrics according to applications
Results for best methods of each team
ACO
ARG
GARAC
CNN
T40
T50
FLAB
0.4 × PPV + 0.6 × SE (RT planning)

## Slide 43: PET segmentation challenge
Metrics according to applications
Results for best methods of each team
ACO
ARG
GARAC
CNN
T40
T50
FLAB
0.6 × PPV + 0.4 × SE (Therapy follow-up)

## Slide 44: PET segmentation challenge
Comparison according to other metrics
Dice
ACO
ARG
GARAC
CNN
T40
T50
FLAB
Results for best methods of each team

## Slide 45: PET segmentation challenge
Comparison according to other metrics
Jaccard
ACO
ARG
GARAC
CNN
T40
T50
FLAB
Results for best methods of each team

## Slide 46: PET segmentation challenge
Overall observations
  All 4 methods performed well
    Significantly better than both fixed thresholds
      (0.75-0.85 for teams vs. <0.6 for thresholds, p<0.0001)
    Only one method (CNN) significantly outperformed state-of-the-art FLAB method (p=0.0007)
  The methods performance decreases with the reliability of the ground-truth / realism of data
    Simulated data > phantom acquisitions > clinical images
Discussion

## Slide 47: PET segmentation challenge
Overall observations
  The results highlighted a clear hierarchy
    which does not depend strongly on either
      type of dataset (except for clinical data for which the differences are less pronounced)
      or metric used
      or applications (favor SE or PPV)
Discussion
Rank | Method | Significant?
1 | CNN (team 4) | 
2 | ACO (team 1) | 
3 | ARG (team 2) | 
4 | GARAC (team 3) | 
Yes*
Yes***
Yes*
SE+PPV, Jaccard, Dice
Yes***

## Slide 48: PET segmentation challenge
M. Hatt, et al. The first MICCAI challenge on PET tumor segmentation. Medical Image Analysis 2018
Results
  Ensemble techniques

## Slide 49: PET segmentation challenge
Runtime (for the 149 testing data)
Results for best methods of each team
 | Mean | ACO | ARG | GARAC | CNN
Runtime (min) | 6h00 | 4h04 | 9h20 | 3h39 | 7h00
Relative Runtime (%) | 1 | 0,67 | 1,55 | 0,61 | 1,16

## Slide 50: PET segmentation challenge
Limitations and perspectives
  Not evaluated in the challenge:
    Robustness with respect to
      noise levels
        images with # levels of noise
      multicentric data
        images of same object in # scanners
    Reproducibility/repeatability and user-interaction
      multiple runs of pipelines on VIP
      user interaction, manual parameters…
    Numerous other methods!

## Slide 51: PET segmentation challenge
Benchmark extensions
    Addition of methods / metrics
    Addition of recently developed datasets:
B. Berthon, et al. A novel phantom technique for evaluating the performance of PET auto-segmentation methods in delineating heterogeneous and irregular lesions. EJNMMI Phys 2015
CD. Soffientini, et al. Technical Note: A new zeolite PET phantom to test segmentation algorithms on heterogeneous activity distributions featured with ground-truth contours. Med Phys 2017

## Slide 52
Thanks for your attention

## Slide 53: Acknowledgments
Assen Kirov, Emiliano Spezi, John A. Lee, Michalis Aristophanous, Shiva Das, Issam El Naqa, Robert Jeraj, Wei Lu, Osama Mawlawi, Béatrice Berthon, Elisabetta De Bernardi, Charles Schmidtlein, Dimitris Visvikis, Aditya Apte, Paulina Galavis, Andrei Pugachev, Habib Zaidi, Ursula Nestle, Arden Nelson, Heiko Schöder, Michael MacManus, Vincent Grégoire, Xavier Geets
MICCAI challenge
Challengers
Anouar Ouahabi, Hadi Fayad
Vincent Jaouen, Clovis Tauber
Shan Tan, Laquan Li, Wei Lu, Shuaiwei Liu, Xu Huang
Jakub Czakon, Filip Drapejkowski, Witold Dyrka, Piotr Giedziun, Grzegorz Żurek, Jakub Szewczyk, Piotr Krajewski, Jacek Żebrowski
Sponsorship - funding
France Life Imaging (grant ANR-11-INBS-0006 from the French “Investissements d’Avenir” program).
NIH/NCI Grant R01CA172638 and the NIH/NCI Cancer Center Support Grant P30 CA008748
Support Programme of the Partnership between Higher Education and Science and Business Activity Sector financed by City of Wroclaw
Organization
FLI: Christian Barillot, Michel Dojat
FLI-IAM: Baptiste Laurent, Michael Kain, Yao Yao, Mathieu Simon, Aneta Morawin, Julien Louis, Simon Loury
VIP platform: Tristan Glatard, Sorina Camarasu-Pop, Frédéric Cervenansky, Pascal Girard
Other: Federico Turkheimer, Olivier Commowick, Catherine Cheze Le Rest
AAPM TG 211